## Slide 1
Low-Level RF System Development for EIC Crab Cavities
October 15th , 2025
Freddy Severino,
RF Systems Head, Collider Accelerator Department
EIC RF Controls Technical Lead

## Slide 2: Outline
Introduction
EIC Crab Systems Overview
RF Control Specification
  RF Noise
  Impedance
  Crabbing closure
RF Control Hardware
Low-Level RF Control Solution
  RF Noise
  Impedance
RF Control Global Plan
Summary Status

## Slide 3: Introduction
The Electron Ion Collider (EIC) beams will collide with a large (25 mrad) crossing angle to separate electron and proton beam quickly and limit beam-beam effects [1].
The large crossing angle provides space for a neutron detector in the forward hadron direction, and for the luminosity detector in the forward electron direction.
Collisions with a crossing angle reduce the overlap region of the colliding bunches, which reduces the luminosity by an order of magnitude for 25 mrad [1].
The resulting luminosity loss will be largely restored by rotating the bunches around the vertical axis at the IP (perpendicular to the crossing plane) by half the crossing angle using transversely deflecting RF resonators, or crab cavities, in both the hadron and electron rings[1].
  Schematic layout of the interaction region, EIC Conceptual Design Report

## Slide 4: Crab crossing to recover head-on collisions
Crab-cavities:
  Crabs apply head and the tail transverse kick to proton and electron bunches in opposite directions (in the plane of the crossing angle).
  Correct for crossing angle effects
  Restore head-on collision
  Achieve maximum luminosity
  S.U. De Silva et. al. MOPAB393 IPAC2021 (2021)
Without
Crabbing
With
Crabbing

## Slide 5: EIC Crab Cavity Overview
Crab Cavities (IR6) | HSR (Cavities/CMs) | ESR (Cavities/CMs)
197 MHz | 8/4 | –
394 MHz | 4/4 | 2/2*
*or 4/4 for redundancy
HSR: Hadron Storage Ring
ESR: Electron Storage Ring
For 197MHz crab cavity
Operating voltage per cavity: 8.5 MV.
Designed specs: 11.5MV per cavity.
2 cavities in 1 cryomodule.
N. Huque
5
Binping Xiao
Notes: Low in freq -> large in size, geometric constraint/mechanical design/fabrication/surface treatment/installation.
Tight impedance budget, high HOM power -> difficulties in damper designs.
for EIC, the longitudinal impedance budget is two orders of magnitude lower comparing with HL-LHC for 197MHz and three or-ders of magnitude lower for 394MHz, while the transverse impedance budget is one order of magnitude lower for both 197MHz and 394MHz.
Due to the high current and short bunch length, especially for electron bunch, the HOM power of both 197MHz and 394MHz systems are high while comparing with HL-LHC.

## Slide 6: EIC 197 MHz Crab Cavity
Two field probes designed to extract 5 W each at 11.5 MV.
One FPC port
47 kW with 50 Hz microphonics and 0.6 mm beam offset, 1.75e6 FPC Qext, 11.5 MV crabbing voltage, 1 A beam.
RF Property | Value | 
Vt [MV] | 8.5 | 11.5
Ep [MV/m] | 33.2 | 44.9
Bp [mT] | 60.1 | 81.3
Total Vt [MV] | 34 | 
No. of cavities | 4 | 3
Operating Temp. [K] | 2.05 | 
Stored Energy [J] | 50.3 | 92
Rs [Ω] (RBCS = 0.4 nΩ) | 15 | 
Pdiss [W] | 9.6 | 17.6
Q0 (G = 97.2 Ω) | 6.48×109 | 
S. De Silva
6

## Slide 7: Crab RF Specification: Impedance Reduction
Impedance Reduction Crab RF Systems:
The fundamental mode of the crab cavity presents a large transverse impedance.
The large transverse impedance coupled with large beta can lead to very strong transverse instabilities [2,3].
Feedback Gain to reduce cavity impedance:
  High-gain feedback (68 dB).
  One-turn delay (20 dB) @ betatron side-bands.
  88 dB total impedance reduction required [1,2].
Fc | 197 MHz
Cavity Impedance | 4.2e9 Ohms/m
Qext | 1.75e6
RoverQ | 2400 ohms/m Cir Def
Effective Q | 300
Fast-Feedback | Gain ~ 3000.
Themis Mastoridis

## Slide 8
RF VOLTAGE ERROR IMPACTS TILT ANGLE
RF PHASE ERROR BEAM TRANSVERSE CENTER OFFSET AT THE IP
S. Verdú-Andrés (BNL) | Crab Cavities for Colliders
0
0
At the IP:
0
0
At the IP:
Full overlap
Partial overlap
Over or under compensation of crossing angle prevents full head-on recovery
eads to a shift on bunch centroid position
Effect of Crab System’s RF noise
Notes: A crab cavity is just a deflecting cavity operated in zero-voltage crossing phase; any phase error makes the crab cavity impart a combined crabbing plus deflecting kick.
Fast phase modulations (100 ps peak to peak) will introduce sinusoidal bunch distortions.
0.007 deg = 1e-4 rad for KEKB crab cavity system (see Morita’s talk)

## Slide 9: Crab RF Specification: Field Regulation
The stability requirement varies in different accelerator.
The requirement on amplitude / phase stability differs by time scale, short term, medium term, long term (minutes to hours). It is often specified as an rms value but peak to peak is also used.
HSR Crab Systems stability requirements? Under development
Target (HSR 275 GeV) 
 | XFEL (RF 1.3 GHz) | ILC (RF 1.3 GHz) | SNS (RF 402.5 MHz) | JPARC Multiple | CeCPoP Multiple
Amplitude/Phase Stability | 0.01%, 0.0 (rms) | 0.1%, 0. (rms) | 0.5%, 0. | 1%, | 0.01%, 0. (rms)
 | XFEL (RF 1.3 GHz) | ILC (RF 1.3 GHz) | SNS (RF 402.5 MHz) | JPARC Multiple | CeCPoP Multiple
Amplitude/Phase Stability |  |  |  |  | 
 | HSR 275 GeV (197 MHz Crab)
Amplitude/Phase Stability | ~0.001%, ~0.000 (rms) Integrated +/- 1kHz around each betatron sideband offset from carrier
 | HSR 275 GeV (197 MHz Crab)
Amplitude/Phase Stability | 

## Slide 10: RF Noise Specification: Crab RF Systems
RF Noise (Field regulation):
RF noise increases the transverse emittance which reduces the luminosity.
  Phase noise kicks leads to a shift on bunch centroid position.
  Amplitude noise leads to a rotation of the bunch.
The sensitivity of RF noise is particularly high in the HSR Crab RF systems.
  This is the most challenging aspect of the Low-Level RF design.
  The RF noise threshold for the HSR will be very hard to achieve technologically
LLRF Design Requirements:
  The target phase noise was set @ < -151 dBc/Hz integrated +/- 1 kHz around each betatron sideband.
  This noise level is at the limit of current state of the art.
RF Noise feedback is required:
  A noise cancelation system will also be required achieve the emittance growth rate target due to RF noise equal to the IBS growth rate expected which about 1 / 2 hr for 275 GeV.

## Slide 11: Other Crab RF Specification
Expected transient beam loading effects [5]:
  Residual offset on beam transverse position.
  Reduce luminosity.
  Higher RF power amplifier peak power (Gain)
  The transient beam loading in crabs leads to very small effect on ∆XIP [5].
Strict regulation (Amplitude / Phase):
  0V set-point during injection, ramping.
  Ramp-up voltage at Store.
  Vector sum regulation.
  Crabbing vs Un-crabbing voltage & phase
Themis Mastoridis

## Slide 12: RF Field Control Based on RHIC LLRF
RHIC RF Systems (28 MHz & 197 MHz) NCRF:
Capture, Acceleration and Store in RHIC.
Field control feedback loop:
  Digital Low-Level RF Controller
    NCO FPGA
    RF DAC
    RF ADC
    Digital LLRF feedback for long term stability
  Analog direct RF feedback
    46 dB of gain (x200) for impedance reduction.
    Gain is limited by Cavity parameter & Loop delay.
Resonance control:
  Fast ferrite tuner (28 MHz)
  Slower mechanical tuner for acceleration ramp.
A Vector Network Analyzer (VNA) is used for setting up direct feedback loop stability.
Field regulation and phase noise are primarily determined by the quality of the LLRF drive (Loop Reference).
  (j

## Slide 13: C-AD LLRF (Field Regulation)
RF Field noise on 28 MHz cavity with 46 dB of direct-feedback gain:
  Phase noise on cavity field identical to noise out from LLRF RF drive.
  No measurable difference was found for all other RHIC RF systems.
LLRF drive (loop ref) :
~ 240 fsec (0.002 @ 28 MHz) (1 Hz to 10 kHz)
Cavity field :
~ 240 fsec (1 Hz to 10 kHz)

## Slide 14: EIC Low-Level RF Control hardware overview
LLRF design is based on the EIC common platform hardware design
  Common general purpose carrier
  Function-specific daughtercards
  Common timing data link Line rate 8 Gbps​
  Standard control system interface
  100 MHz Master Clock
EIC common platform hardware is an evolution of RHIC Low-level RF platform used in C-AD since 2009.
  FPGA based carrier card
  Gigabit serial link (deterministic / low-latency) timing and data communication
  Use function-specific daughtercards
Major Hardware Components:
  Analog Up/Down Converter & LO Generation
  Low-Level RF daughter cards (RF ADC/RF DAC)
  Resonance & Interlock Design
  Common platform carrier
  Extended Carrier
  Timing data link (TDL)
  Digital IO Card
  Based band ADC
Kevin Mernick

## Slide 15: Perturbations on real world RF system
Low-Level RF:
  Master clock phase noise.
  Clock jitter, nonlinearity on components.
  DAC & ADC additive jitter.
  Crate power supply ripple.
High Power RF:
  Additive noise.
  Amplifier power supply ripple.
  Amplifier Nonlinearities.
Cavity:
  Microphonics induce detuning.
  Lorentz force detuning.
  Thermal effects (Quenching).
  Field Multipacting.
Beam induced:
  HOMs, wake-field.
  Changes on beam spectrum.
  Transient beam loading.
Cross-talk between signals.
Temperature drift.
𝑉(𝑡)) = 𝑉𝐶𝐴𝑉[1 + α(𝑡)] × sin⁡[𝜔𝑅𝐹(𝑡) + ϕ(t)]
Direct Digital Synthesis (DDS)
RF Amplifier

## Slide 16: EIC Crab Cavity Low-Level RF Solution
Design effort focus in five areas:
Master clock (RF Noise)
  Generation
  Distribution
  Conditioning
Digital Controller (RF Noise)
  Low Noise LLRF drive (DDS).
  Low Noise Digitizer (RF ADC)
  OTFB reduce impedance (20dB)
  Cavity protection (Quench)
  Vector Sum Control
  Cavity trip recovery
Direct-rf feedback (RF Noise).
  Reduce Impedance (Gain = 68 dB)
  Low-Noise vs High-gain.
  RF Amplifiers RF Noise/Linearity.
  Power Limiter.
  Cavity quench protection
Each side of IR6
  Phase reference line.
  Beam phase pickup.
Head/Tail measurement system (Instrumentation):
  Noise cancelation FB Term
  Crabbing closure term
Cable bundle
Multi-ADCs (Noise)
Notes: Crab Cavities Building (keep delay short).
Crabbing closure term from Head/Tail measurement high precision BPMs and ADCs (Manfred, Dave, Themis)

## Slide 17: Master Clock Distribution
100 MHZ Master Clock Generation
IR10: Clock Receiver, Clean-Up, Drift Comp
17
Crabs
Crabs
Crabs

## Slide 18: RHIC Master Clock
RHIC Master Clock
RF Phase noise RHIC Master Clock
Good close-in phase noise ~100 fsec rms jitter (1 Hz to 100 kHz)
RHIC Master clock phase noise mostly preserved when transmitted over fiber.
-150 dBc/Hz noise floor limit on fiber transition/recovery is acceptable for RHIC but not sufficient for EIC Crab RF Systems.
18

## Slide 19: EIC Master Clock
EIC Master Clock source:
Very-Low Phase Noise (close-in and noise floor)
  RMS Jitter: better than 50 fsec (1 Hz to 100 MHz)
Thermally stabilized
GPS Disciplined Rubidium Oscillator
Commercially available
Distribution over fiber to each service building
  Timing Data Link system
19

## Slide 20: LLRF Digital Controller: DDS
Most modern Low-Level RF implement Direct Digital Synthesis (DDS):
  FPGA based numerical controlled oscillator (NCO)
  Integrated PLL for clock clean up (RHIC,EIC)
    On Board High Frequency VCO
    On Board PLL IC (RHIC AD9510, EIC CP LTC6952)
    Selectable Clock Output Frequency
    Low Cost (every board)
  Digital to Analog Converter (DAC)
    Low latency, 16 Bits parallel interface (feedback)
    Older technology
    Good trade-off noise performance, clock speed & latency
      RHIC DAC (MAX5891) - 600 MSPS
      EIC CP DAC (AD9783) most applications – 500 MSPS
20
EIC CP DAC @ 197 MHz (LTC6952 PLL & AD9783)
RHIC LLRF @ 197 MHz (AD9510 PLL & MAX5891)
Notes: 1) Far from target using RHIC LLRF or Common platform DAC & New On-Board PLL.

## Slide 21: LLRF Digital Controller: Crabs DDS
EIC Crab Cavity Low-Level RF:
  FPGA based numerical controlled oscillator (NCO)
  Digital to Analog Converter (DAC)
    High Speed RF DAC (AD9164): 16 Bits, 12 GSPS
    New technology
    Improved phase noise performance vs parallel DACs
    Requires High Speed Clock
  Dedicated Clock Receiver Board
    Ultra-low Noise 100 MHz VCO
    Low-Noise clock multipliers
    Low-Bandwidth Lock to reference clock
    One for each (Crab building)
21
Notes: One high end VCO for clock recovery, Up to 2 for each crab cavity building.

## Slide 22: Crabs DDS: External clock receiver PLL
22
EIC Crab Cavity Low-Level RF:
  FPGA based numerical controlled oscillator (NCO)
  Digital to Analog Converter (DAC)
    High Speed RF DAC (AD9164): 16 Bits, 12 GSPS
    New technology
    Improved phase noise performance vs parallel DACs
    Requires High Speed Clock
  Dedicated Clock Receiver Board
    Ultra-low Noise 100 MHz VCO
    Low-Noise clock multipliers
    Low-Bandwidth Lock to reference clock
    One for each (Crab building)
c/o M. McCooey
Notes: One high end VCO for clock recovery, Up to 2 for each crab cavity building.

## Slide 23: Crabs DDS Preliminary Results
Preliminary results LLRF Drive:
Hardware Setup:
High speed DAC (AD9164) Eval board
RHIC 100 MHz Master clock (Tx Fiber)
Clock Receiver Board
  Ultra-low Noise 100 MHz VCO
  Low-Bandwidth Lock to reference clock
  Low-Noise Clock Multipliers
  2 GHz Clock to DAC Eval
Lab Results:
RF noise is on target requirement Crabs LLRF Drive
~50 fsec 1Hz to 10 kHz
~6 fsec 10 kHz to 1 MHz
Further improvements planned final design:
Select better clock multiplier (Wenzel vs Mini Circuits)
Improve board regulator design
Combine multiple DDS outputs
  Doubling DSS (3 dB improvement).
23
c/o M. McCooey & S. Mai

## Slide 24: Direct-rf feedback (RF Noise)
Direct-rf feedback RF noise:
Feedback gain 68 dB (6000)
  Much higher than RHIC systems (@46dB)
RF Amplifier chain gain 100 dB (x 100 K)
  Similar to RHIC 197 MHz (@ 93 dB)
Driver Amplifiers noise factor is more critical
  RF chain noise factor is primarily established by noise figure of its first amplifying stage.
  Friis’s Formula:
  1st Driver noise becomes loop reference
    Filtered by Cavity closed response.
    Feedback corrects in-band noise.
  2nd Driver noise is amplified (OL)
    Signal closer to noise floor
    Filtered by Cavity Open Loop
High Power RF Amplifier design
  Design in house (RHIC 197 MHz)
  Linearity
  Regulators
  Under evaluation
Closed Loop
68 dB
250 ns loop delay
Open Loop TF
LLRF Drive / Loop Ref
Cavity RF noise reduced CL (~10dB)
Notes: Amplifier chain forward gain is similar to that of the RHIC 197 MHz (93 dB vs 100 dB) (Ratio FPC Power to Pickup Power)
The feedback enforces RF noise on the loop reference (within loop Bandwidth).
Noise on the reference is only filtered by Closed loop response.
Noise on amplifier inside the loop is filtered by cavity open loop response.
Very Low noise Figure driver amplifiers are available used for clock distribution applications

## Slide 25: OTFB (RF Noise): Digitizer
OTFB Implementation:
  Implemented on the FPGA.
  Wide band to cover many revolution line.
  Track betatron frequencies during the ramp.
  RF ADC additive noise is a concern
    Typical : ~ 77 dB SNR @ 125 MSPS
    Additive noise ~ - 152 dBc/Hz
OTFB:
Double Comb
Betatrond Side band
OTFB RF ADC Noise Improvement:
EIC RF ADC design in progress
Provide direct clock (on-Board PLL bypassed)
Down Convert &/or Analog I&Q demodulator (Improves Noise)
Average multiple ADC channels
RF ADC Phase Noise Measurement (RHIC RF ADC)
Matlab Script developed by CAD LLRF Engineer : Michael McCooey
RHIC RF ADC ~ -152 dBc/Hz

## Slide 26: Crab Cavity LLRF: Hardware
Noise cancelation feedback system:
Dedicated high precision beam pickup
  Reduce RF systems noise
  Correct Crabbing vs Un-crabbing decidual error
Vector Sum Controller restores voltage/phase on each side of the IR (May pull beam permit)
HL RF Trip:
Beam Permit
EIC Instrumentation

## Slide 27: Summary & Status
Design effort focus in five areas:
Master clock (RF Noise)
  Generation
  Distribution
  Conditioning
Digital Controller (RF Noise)
  Low Noise LLRF drive (DDS).
  Low Noise Digitizer (RF ADC)
  OTFB reduce impedance (20dB)
  Cavity protection (Quench)
  Vector Sum Control
  Cavity trip recovery
Direct-rf feedback (RF Noise).
  Reduce Impedance (Gain = 68 dB)
  Low Noise RF Driver Amplifier.
  RF Amplifiers RF Noise/Linearity.
  Power Limiter.
  Cavity quench protection
Each side of IR6
  Phase reference line.
  Beam phase pickup.
Head/Tail measurement system (Instrumentation):
  Noise cancelation FB Term
  Crabbing closure term
Cable bundle
Multi-ADCs (Noise)
Demonstrated solution meets requirements (operational or evaluation board)
In progress
Multi-DACs (Noise)
Notes: Crab Cavities Building (keep delay short).
Crabbing closure term from Head/Tail measurement high precision BPMs and ADCs (Manfred, Dave, Themis)

## Slide 28: Acknowledgements
JLab & BNL (EIC & C-AD) RF teams (former and present).
  Michael McCooey , Geetha Narayan, Kevin Mernick, Arshdeep Singh
  Samson Mai, Mark Hoffmann Wallner, Alex Zaltsman, Michael Sowinski
  Binping Xiao, Silvia Verdu Andres and many others
  Special thanks to Michael McCooey for his work on clock recovery/clean-up and RF noise measurements
Michael Blaskiewicz provided Accelerator Physics support.
Themis Mastoridis for his support providing analysis of RF systems challenges.
Thank You !
Questions ?

## Slide 29
References
  [1] F. Willeke et al., “Electron-Ion Collider conceptual design report,” BNL, Upton, NY, USA, Feb. 2021.
  [2] M. Blaskiewicz, Instabilities Driven by the Fundamental Crabbing Mode, BNL Tech Note BNL-222221-2021-TECH
  [3] T. Mastoridis, M. Blaskiewicz, and T. Loe, Eic transverse instabilities due to the crab cavity fundamental impedance, Accepted for publication to Phys. Rev. Accel. Beams (2024).
  [4] K. Smith, T. Mastoridis, P. Fuller, P. Mahri, and Y. Matsumura, EIC transverse emittance growth due to crab cavity RF noise: Estimates and mitigation,, BNL-222748-2022-TECH
  10.2172/1846026 (2022).
  [5] T. Mastoridis, etc all, “Time-domain simulation of the crab cavity/beam interaction ”, BNL Tech Note BNL-224087-2023-TECH EIC-ADD-TN-039.

## Slide 30
Themis:
#11, Power for zero voltage set-point during the energy ramp
What is new compared to RHIC: Noise req, High Q cavity with Higher gain.
Can we fix the bandwidth or make it changeable (Gain changes)
OTFB loop we could turn-it off at Store to keep noise off.

## Slide 31: Questions

## Slide 32: Backup Slides

## Slide 33: Amplitude Noise AD9164 Eval Board

## Slide 34: Low Level RF Controller: Functions
Core LLRF functions:
  Generates LLRF Drive.
  Regulates Cavity RF field’s amplitude and phase.
  Resonance control.
  Cavity protection.
  Provides control system interface.
  Provides calibrated measurements of all cavities waveform (Forward, Reflected, Probe).
LLRF Interacts:
High Power RF
Couplers
Cavity and Cavity tuners
Cryogenics
Controls
Cooling Systems
Beam
Experiments
Cavity as an Electrical System
2nd Order Band-pass
filter
𝑉(𝑡)) = 𝑉𝐶𝐴𝑉(𝑡) × sin⁡[𝜔𝑅𝐹(𝑡)]

## Slide 35: RF phase Noise: Move to back-up
Phase noise is the frequency-domain representation.
  Short-term random fluctuations in the phase of a signal.
  Spreads out equally on either side of the carrier but only one side is measured.
While specifying phase noise, three elements need to be specified:
1. Phase Noise Amplitude: It is expressed in dB relative to the carrier. This is normally denoted in dBc/Hz, e.g. -70 dBc - 70 decibels down in level from the carrier.
2. The offset from the carrier: Ex. 1 kHz, 10 kHz, 100 kHz.
3. Measurement bandwidth: Noise power is proportional to the bandwidth so it should be always mentioned. Typically 1 Hz is taken as the bandwidth.

## Slide 36: Crab RF Specification: Field Regulation ??
The stability requirement varies in different accelerator.
The requirement on amplitude / phase stability differs by time scale, short term, medium term, long term (minutes to hours). It is often specified as an rms value but peak to peak is also used.
HSR Crab Systems stability requirements? Under development
Target (HSR 275 GeV) 
 | XFEL (RF 1.3 GHz) | ILC (RF 1.3 GHz) | SNS (RF 402.5 MHz) | JPARC Multiple | CeCPoP Multiple
Amplitude/Phase Stability | 0.01%, 0.0 (rms) | 0.1%, 0. (rms) | 0.5%, 0. | 1%, | 0.01%, 0. (rms)
 | XFEL (RF 1.3 GHz) | ILC (RF 1.3 GHz) | SNS (RF 402.5 MHz) | JPARC Multiple | CeCPoP Multiple
Amplitude/Phase Stability |  |  |  |  | 
 | HSR 275 GeV (197 MHz Crab)
Amplitude/Phase Stability | ~0.001%, ~0.000 (rms) Integrated +/- 1kHz around each betatron sideband offset from carrier
 | HSR 275 GeV (197 MHz Crab)
Amplitude/Phase Stability |